## Slide 1
PeatGuard
Satellite-Based Peatland Subsidence Monitoring
for Carbon Credit MRV in West Kalimantan, Indonesia
Tommy Quak
National University of Singapore, Department of Geography
March 2026

## Slide 2
The Problem: Tropical Peatland Carbon Crisis
Indonesia's 20.6M hectares of peatland store 88.6 Gt carbon -- equivalent to a decade of global fossil fuel emissions (Page et al., 2011)
Drainage for oil palm has converted 5.1M hectares, releasing 0.9-1.4 Gt CO2/year (Hooijer et al., 2010)
Drainage triggers irreversible peat oxidation and compaction, manifesting as measurable land surface subsidence
Subsidence rates: 40-60 mm/yr in first 5 years, declining to 20-30 mm/yr over decades (Hooijer et al., 2012)
Carbon credit market opportunity: USD 5.78B for peatland rewetting under Verra VCS VM0007
Challenge: How to measure, report, and verify peat degradation at landscape scale for carbon credits?

## Slide 3
Why InSAR? Rationale for Sensor Selection
Why Sentinel-1 C-band SAR
Only satellite technique measuring mm-level ground displacement from space
All-weather, day-night: critical for tropical Kalimantan (200+ cloud days/yr)
Free and open data (Copernicus Programme) -- ensures reproducibility and continuity
12-day repeat cycle provides sufficient temporal sampling for SBAS time-series
Subsidence IS the physical signal of peat carbon loss -- direct measurement, not a proxy
Why NOT optical / hyperspectral
Optical sensors (Sentinel-2, Landsat) cannot measure ground displacement
NDVI detects vegetation stress but not the subsidence that drives it
Hyperspectral (PRISMA, EnMAP) identifies surface chemistry, not vertical motion
Cloud cover in Kalimantan blocks optical sensors >200 days/yr
Optical data used for validation (Hansen GFC, NDVI) not primary measurement

## Slide 4
System Architecture: Cloud-Native InSAR Pipeline
5-stage pipeline deployed on Google Cloud Platform (Cloud Run Jobs):
Stage 1: Data Ingestion -- 14 Sentinel-1 SLC + 14 GRD scenes from ASF DAAC (Jan-Dec 2024)
Stage 2: InSAR Processing -- ISCE2 topsApp, 29 SBAS pairs, SNAPHU MCF unwrapping, ionospheric correction
Stage 3: Time-Series Analysis -- MintPy SBAS inversion, ERA5 tropospheric correction, MintPy geocoding
Stage 4: Backscatter Processing -- GRD calibration, Lee Sigma speckle filter, terrain correction, temporal median
Stage 5: Analysis -- Canal detection, water masking, classification, risk scoring, carbon loss, Hansen integration
Fully containerised (Docker), automated monthly (Cloud Scheduler + Workflows), open-source on GitHub

## Slide 5
Key Scientific Decisions and Rationale
Decision | Choice | Rationale | Reference
Subswath | IW2 (not IW3) | IW3 gave 45% pair failure; IW2 provides full AOI burst coverage | ASF burst analysis
Multilooking | 3 az x 9 range | Reduces phase noise 5.2x while preserving canal-scale features (~42x21m) | Standard for S-1 IW
Unwrapping | SNAPHU MCF | Minimum cost flow handles smooth deformation fields in low-coherence tropics | Chen & Zebker 2002
Atmos. correction | ERA5 via PyAPS | Removes 5-15 mm/yr tropospheric bias; two-phase reference selection | Jolivet et al. 2014
LOS-to-vertical | cos(37) factor 1.25x | Peat subsidence is purely vertical; Sundaland horiz. motion <1 mm/yr | Simons et al. 2007
Coherence mask | 0.5 threshold | Excludes noisy forest pixels; 0.3 too permissive for tropical C-band | Hoyt et al. 2020
Canal detection | 10th pctl threshold | Captures water-filled canals via specular reflection; 9.1% coverage | Validated vs OSM
Risk weights | 0.45 prox + 0.55 sub | Direct measurement (subsidence) weighted higher than proxy (canal distance) | Hooijer et al. 2012
Carbon factor | 0.5 tCO2/ha/yr/mm | Conservative estimate from Hooijer; some studies report 0.7-1.0 | Hooijer et al. 2012

## Slide 6
ERA5 Tropospheric Correction: Why It Matters
Problem: Tropical water vapour causes 5-20 mm equivalent phase delay per acquisition
Without correction: velocity bias of 5-15 mm/yr (up to 50% of the subsidence signal)
Solution: Two-phase ERA5 reference selection strategy:
Phase 1: Run MintPy WITHOUT ERA5 to select reference point on uncorrected data
Phase 2: Lock reference point, re-run WITH ERA5 atmospheric correction
Why two phases? ERA5 changes the phase pattern, which can shift the auto-selected reference
point to subsiding ground, introducing a +35 mm/yr false positive bias
Result: ERA5 correction removes atmospheric noise while preserving the correct velocity datum
15/15 acquisition dates corrected using ECMWF ERA5 pressure-level reanalysis (Hersbach et al., 2020)

## Slide 7
Results: Subsidence and Carbon Loss
Metric | Value | Interpretation
Mean vertical velocity | -26 mm/yr | Consistent with Hooijer (2012): 20-50 mm/yr for drained peat
Severe subsidence (<-50) | 30% of area | Heavily drained peat near primary canals
Active drying (-50 to -20) | 11% of area | Ongoing drainage impact, significant CO2 loss
Moderate drying (-20 to -5) | 6% of area | Slow but measurable carbon loss
Stable (-5 to +5) | 4% of area | Within natural variability
Canal network coverage | 9.1% | Detected via VV backscatter thresholding
Water bodies detected | 1.1% | Kapuas River and ponds (VV dB < -18)
Mean risk score | 0.48 | Moderate-to-elevated across drained landscape
Peat extent coverage | ~60% of AOI | From WRI/GFW Indonesia peatland dataset

## Slide 8
Carbon Loss Estimation
Conversion: CO2 loss (tCO2/ha/yr) = |subsidence velocity (mm/yr)| x 0.5
Based on Hooijer et al. (2012) empirical relationship for Indonesian tropical peat
Conservative factor (0.5); literature range is 0.5-1.0 depending on drainage age
Quality filters applied before carbon estimation:
- Coherence > 0.5 (excludes unreliable pixels under forest canopy)
- Water mask applied (excludes rivers and ponds)
- 5x5 median filter (reduces pixel-level noise)
Carbon-loss-backed visualization thresholds:
0-1 tCO2/ha/yr: Natural variability
1-5: Drainage-affected
5-10: Active degradation
10-20: Severe degradation
>20: Critical emission hotspot

## Slide 9
Error Budget: Quantified Uncertainty
Error Source | Magnitude | Mitigation | Status
Tropospheric delay | 5-15 mm/yr | ERA5 correction (PyAPS) | Corrected
Ionospheric delay | 2-5 mm/yr | Split-spectrum (ISCE2) | Corrected
Reference point | 3-8 mm/yr | Two-phase selection | Mitigated
Temporal decorrelation | 2-10 mm/yr | Coherence mask (0.5) | Partially mitigated
Unwrapping errors | 0-28 mm/yr per event | SNAPHU MCF + SBAS network | Mitigated
LOS-to-vertical | <3 mm/yr | Constant incidence (37 deg) | Applied
Georeferencing | ~100 m | MintPy geocoding | Corrected
Seasonal aliasing | 5-15 mm/yr | 1-year span (limitation) | Not yet corrected
Total RSS | ~8-12 mm/yr |  | 30-46% relative uncertainty

## Slide 10
Validation Strategy
Internal Consistency
Velocity vs canal distance: r = -0.40 (p < 0.001) -- subsidence correlates with drainage proximity
Velocity vs VV backscatter: r = 0.27 (p < 0.001) -- cleared areas show more subsidence
Mean velocity (-26 mm/yr) matches published rates for drained Indonesian peat
Classification distribution is physically plausible (47% subsiding, 4% stable)
External Datasets
Hansen GFC: clearing-year cohort analysis validates temporal subsidence pattern
OSM waterways: precision/recall against community-mapped canal features
WRI peat extent: subsidence concentrated within mapped peatland boundaries
Limitation: No ground truth (GPS, levelling, piezometers) available in study area

## Slide 11
Honest Limitations
C-band cannot penetrate forest canopy: ~45% of pixels are low-coherence (masked at 0.5)
- This means we cannot measure subsidence under intact peat forest
- L-band (ALOS-2 or NISAR) would address this gap
Single-year temporal coverage (2024): seasonal aliasing adds 5-15 mm/yr uncertainty
- Extending to 2+ years enables seasonal decomposition
No in-situ ground truth: all validation is against remote sensing datasets
- Planned: collaboration with Tanjungpura University for piezometer data
Peat depth is estimated (dome model), not measured
- CIFOR peat map provides extent; depth classification is approximate
Carbon loss factor (0.5 tCO2/ha/yr per mm/yr) is an empirical average, not site-specific

## Slide 12
Future Development Roadmap
Phase 1: Immediate (1-2 weeks)
Extend to 2+ years of data (2023-2024) for seasonal decomposition and noise reduction
Apply for ALOS-2 L-band data (JAXA EORC, free for NUS students)
Add Sentinel-2 NDVI composite for land cover classification
Implement unsupervised K-means clustering for degradation zone mapping
Confidence mapping: per-pixel quality indicator from coherence + uncertainty
Phase 2: Medium-term (1-3 months)
ALOS-2 L-band InSAR for forest-penetrating subsidence (fills 45% canopy gap)
Multi-sensor C+L band fusion: coherence-weighted velocity combining both wavelengths
NISAR integration when data becomes available (free, open access)
U-Net canal segmentation trained on Google Earth + OSM labels
Supervised restoration priority model (Random Forest with expert labels from field visits)
Before/after monitoring for canal blocking effectiveness (Verra MRV requirement)
Web dashboard deployment (TiTiler + Leaflet for live monitoring)

## Slide 13
Machine Learning: Where It Helps vs Where It Doesn't
Application | ML Benefit | Status | Recommendation
K-means degradation zones | Discovers natural spatial patterns, no labels needed | Ready to implement | YES -- immediate
U-Net canal segmentation | Learns grid patterns, reduces false positives | Needs training labels | YES -- 2-3 weeks
Random Forest restoration priority | Multivariate feature fusion with expert knowledge | Needs field data | YES -- with field visit
InSAR velocity estimation | Cannot improve physics-based measurement | N/A | NO -- use MintPy
Atmospheric correction | Cannot improve ERA5 physics-based approach | N/A | NO -- use ERA5
Subsidence classification | Would just re-learn the Hooijer thresholds | N/A | NO -- use thresholds

## Slide 14
Technology Stack
InSAR Processing: ISCE2 (JPL) -- topsApp for Sentinel-1 TOPS, stripmapApp for NISAR L-band
Time-Series: MintPy (University of Miami) -- SBAS inversion, ERA5 via PyAPS, geocoding
Unwrapping: SNAPHU (Stanford) -- Minimum Cost Flow algorithm
Geospatial: GDAL, rasterio, geopandas, scikit-image, scipy
Cloud: Google Cloud Platform -- Cloud Run Jobs, Cloud Storage, Cloud Build, Workflows, Scheduler
Container: Docker (mambaforge + conda-forge for reproducible geospatial environment)
Config: Pydantic v2 models + YAML, environment variable overrides
Data: ASF DAAC (Sentinel-1), CDS (ERA5), Hansen GFC, WRI peatlands, OSM waterways
Output: Cloud-Optimised GeoTIFFs (COG) compatible with ArcGIS Pro, QGIS, web tile servers
Open source: github.com/tommyquak/peatguard-v3

## Slide 15
PeatGuard
Satellite monitoring for peatland restoration and carbon credit MRV Key numbers: 47.5% of study area shows active subsidence Mean vertical subsidence: -26 mm/yr (ERA5-corrected) 9.1% canal network detected from SAR backscatter 19 GeoTIFF products deployed to cloud in <1 hour Tommy Quak | NUS Geography | github.com/tommyquak/peatguard-v3